| Thick Film Chip Resistors |  |
| --- | --- |

Category Type Features Power Rating(W) Resistance Range(Ohm) Tolerance (%) PDF Thick film RK73B General purpose 0.03 1 1 22M 2, 5 RK73H Precision 0.03 1 1 10M 0.5, 1 RK73G High precision 0.05 0.25 10 1M 0.5, 1 RK73Z Jumper chip — 50m max. — RK73A Audio circuit 0.1 0.25 2.2 1M 2, 5 WK73 Wide terminal 0.75 1.5 10m 1M 1, 5 HV73 High voltage 0.1 1 10k 51M 0.5, 1, 2, 5 SG73 Surge・Pulse 0.1 1 1 1M 10, 20 SG73S Surge(Precision) 0.2 0.5 1 10M 0.5, 1, 2, 5 SG73P Pulse(Precision) 0.2 0.5 1 10M 0.5, 1, 2, 5

| Anti Sulfuration Chip Resistors |  |
| --- | --- |

Category Type Features Power Rating(W) Resistance Range(Ohm) Tolerance (%) PDF Thick film (Anti Sulfuration) RK73B-RT Anti Sulfuration (General) 0.063 1 1 10M 0.5, 1, 2, 5 RK73H-RT Anti Sulfuration(Precision) 0.063 1 10 10M 0.5, 1 RK73Z-RT Anti Sulfuration(Jumper) — 50m max. — SG73-RT Anti Sulfuration (Surge・Pulse) 0.1 1 1 1M 10, 20

|  | Thin Film Chip Resistors |  |
| --- | --- | --- |

Category Type Features Power Rating(W) Resistance Range(Ohm) Tolerance (%) PDF Thin film RN73 Metal film (Precision) 0.063 0.25 10 1M 0.05, 0.1, 0.25, 0.5, 1 RN73H Metal film (High heat resistance) 0.1 0.25 10 510k 0.05, 0.1, 0.25, 0.5, 1

|  | Chip Resistors for High Frequency Circuit |  |
| --- | --- | --- |

Category Type Features Power Rating(W) Resistance Range(Ohm) Tolerance (%) PDF Microwave SHD Microwave devices (R, C, Module) 0.031, 0.062 22 1k 5

|  | Current Sense Resistors/Low Resistance Resistors |  |
| --- | --- | --- |

Category Type Features Power Rating(W) Resistance Range(Ohm) Tolerance (%) PDF Low resistance SR73 Thick film (Low resistance) 0.1 1 24m 10 0.5, 1, 2, 5 UR73 Thick film (Low resistance, Low T.C.R.) 0.125 1 10m 100m 1 PSB Power shunt (Ultra low resistance) 6 0.75m, 1m 1 PSI Power shunt (Ultra low resistance) 3 1m 4m 1 PSE Power shunt (Ultra low resistance) 3 0.5m, 1m, 1.5m 5 TLR Metal plate (Ultra low resistance) 0.5 2 1m 20m 1 TLRH Current sensing (Low resistance) 1, 2 22m 250m 1 TSL Current sensing (Low resistance) 1 5m 100m 0.5, 1, 5 SL Current sensing (Low resistance) 0.75, 1, 2 3m 22M 0.5, 1, 2, 5 SLN Current sensing (Low resistance, Low T.C.R.) 2 5m 200m 0.5, 1, 5 NPR Power type 1, 2 3.9m 22M 1, 5, 10 CSR Current sensing (4 terminal) 1, 2 5m 50m 0.5, 1 BLR Current sensing (Ceramic Case) 1, 2,15 8m 50m 5, 10 LR72 Custom milliohm resistors 0.25 1 2m 8m 5

|  | Fusing Resistors |  |
| --- | --- | --- |

Category Type Features Power Rating(W) Resistance Range(Ohm) Tolerance (%) PDF Fusible RF73 Fusing resistor 0.063 1 0.2 510 5

|  | Linear P.T.C. Resistors/thermal sensers |  |
| --- | --- | --- |

Category Type Features Power Rating(W) Resistance Range(Ohm) Tolerance (%) PDF Linear LA73 Thick film linear P.T.C. 0.063 0.125 22 10k 5 LT73 Thin film linear P.T.C. 0.1, 0.125 51 51k 2, 5 LT73V Thin film linear P.T.C. 0.1, 0.125 51 22k 2, 5 LP73 Thin film linear P.T.C. (Precision) 0.016 0.063 100 10k 1, 2, 5

|  | Platinum Thermal Sensors |  |
| --- | --- | --- |

Category Type Features Power Rating(W) Resistance Range(Ohm) Tolerance (%) PDF Platinum SDT73H Platinum thin film thermal sensors 0.063 100, 500 0.2, 1 SDT73V Platinum thin film thermal sensors(For Automotive) 0.063 100, 500 0.2, 1

|  | MELF Type Resistors/Cylindrical Chip |  |
| --- | --- | --- |

Category Type Features Power Rating(W) Resistance Range(Ohm) Tolerance (%) PDF Cylindrical RD41 Carbon film (General purpose) 0.125 0.25 1 2.2M 2, 5 RN41 Metal film (Precision) 0.125 1 0.22 5.11M 0.1, 0.25, 0.5, 1, 5 RM41 Metal film (Precision) 0.2, 0.5 0.22 8.2 5 MLT Linear P.T.C. 0.125, 0.25 1k 9.1k 5 CPCN Ceramic resistor 0.5 2 1k 15k 20 CC Jumper — 20m max. —

|  | Resistor Networks/Resistor Array |  |
| --- | --- | --- |

Category Type Features Power Rating(W) Resistance Range(Ohm) Tolerance (%) PDF Network CN Array (Concave) 0.063 0.125 1 1M 1, 2, 5 CN-A Array (Convex) 0.063, 0.125 1 1M 1, 5 CN-K Array (Convex) 0.063 1 1M 1, 5 CN-N Array (Flat terminal) 0.031 10 1M 5 CND Thick film double common (Concave) 0.05, 0.063 22 100k 5 CND-K Thick film double common (Convex) 0.031 47 39k 5 CNB Thick film single common (Concave) 0.063 1k 470k 5 BR BGA resistor network 0.05 10 1k 1 MRGF16 SOP R network 0.031, 0.063 22 2.2M 2, 5 CNN Metal film (Precision) 0.05 1k, 10k, 100k 0.1, 0.25 KPC R/C/D network (Metal film) 50m200m 10 1M 0.1, 0.25, 0.5, 1, 2, 5

|  | Anti Sulfuration Resistor Networks/Resistor Array |  |
| --- | --- | --- |

Category Type Features Power Rating(W) Resistance Range(Ohm) Tolerance (%) PDF Anti Sulfuration Network CN-RT Anti Sulfuration Resistor Array (Concave) 0.063 0.125 10 1M 5 CN-KRT Anti Sulfuration Resistor Array (Convex) 0.063 3 1M 5

Common Specification Items PDF Minimum Ordered Quantity Recommended Pad Dimensions Packagings for Chip Components Axial Tapings Radial Taping Forming Color code•Resistance marking•E series numbers