αLED Panel  (C-050-6W – 2500k)

Features

High luminous flux per LED

Very long operating life

Available in Warm White, Daylight, and Cool White

More Energy Efficient than Incandescent and Halogen lamps

Low Voltage DC operated

Cool beam, safe to the touch

Instant light (less than 100ns)

No UV

Superior ESD protection

Typical Applications

Reading lights

Decorative

Appliance

Sign and Channel Letter

Architectural Detail

Portable Equipment

Medical Equipment

Automotive Lighting

LCD backlight

C-050- 6W Outline drawing

Parameter

Absolute Maximum Ratings At Ta = 25 ˚C

Power Dissipation 耗電量	6 W

Continuous Forward Current 工作電流	640~680mA

MCPCB Temperature(˚C) 基板溫度	80˚C (Rectangle)

Thermal Resistance (W/˚C) 熱阻

Storage Temperature Range 儲存溫度	–40 ˚C to 100 ˚C

Lead Solder Temperature 260 ˚C for 5 seconds 	廻銲溫度260 ˚C五秒

Operation Time 使用壽命	> 50,000 hours*

Electrical /Optical Characteristics at Ta = 25 ˚C

Symbol	Parameter	Test Condition	Unit	MIN	TYP	MAX

VF	Forward Voltage	IF = 660 mA	V	8.9	9.4	9.9

V	Luminance 	IF = 660 mA	lm	510		550

TC	Color Temperature	IF = 660 mA	K		2500k

Ra	Color–Rendering Index	IF = 660 mA			>70

21/2†	Viewing Angle	IF = 660 mA	deg		> 120

† 1/2 is the off-axis angle where the luminous intensity is half of the on-axis intensity.